## Slide 1: Cache Design Exploration
by Tara K.
Cache Associativity
Conflict Misses
Performance Tradeoffs
A RISC-V cache simulator visually comparing user-defined cache organizations.
Topics Covered:
What is this project?

## Slide 2: Project Structure
GUI
hex_inst.txt
All log files
Actual function (decoder/cache/pipeline/etc)
Used before GUI was created, also useful for debugging
Loader and Logger
Entry Point

## Slide 3: simulator/
Core of the project
Built from the CPU simulator developed through class assignments
Primarily Assignment 6 parameterizing
refactored to handle multiple cache configurations
RISC-V decoder
DMEM lw/sw: ensures cache usage
All stages, stage helpers/traces, and “pseudo-main”

## Slide 4: gui/
New, simple tkinter GUI for visual analysis
CONFIG TAB: Stats for individual configs, and easily visible log files
COMPARISON TAB: Directly compares all provided configs in table/graphs
Check hit rate & hits/misses
Each is its own class

## Slide 5: User Configuration
Designed to be easily configured by user
INPUT_FILE: Custom input path/file
CONFIGS: Cache settings
    Design choice: list[tuple[str, int, int, int]]
  In Assignment 6: NUM_SETS is derived
  In project: cache size is derived
    size = assoc * num_sets * block_bytes
  Easier to get different behavior by specifying assoc and num_sets
NAME
ASSOC:
Number of ways per set – N different blocks occupying the same set
NUM_SETS:
Number of sets in cache – defines how addresses are mapped to cache
BLOCK_BYTES: Data size transferred in one operation

## Slide 6: Demo

## Slide 7: Insights
Conflict Misses
Compulsory
    first time accessing an address
Capacity
    cache size too small, system must evict data
Conflict/Collisions
    addresses mapping to the same set are evicting each other
    Direct-mapped: one address, one cache location
    N-way: addresses get multiple slots before eviction
Performance Tradeoffs
Higher ASSOC:
    Less conflict misses, higher hit rate
    Requires checking more ways
    Performance improvements level off
  Direct-Mapped:
    Only one way, only one search
    High costs for conflict misses, bad hit rate
 | Direct-Mapped | 2-Way | 4-Way
Conflict Miss Cost | High | Medium | Low
Lookup Speed | Fast | Medium | Slow
Hardware Cost | Least | Medium | Most
Hit Rate | Worst | Medium | Best